# IP Packets Deconstructed

Logging onto FTP server from Linux machine

Packet one – captured with Network Sniffer

TCP Port 32769 to 21 SYN window 5840  Seq 93209021  ACK 0

Packet size 60 Protocol 6

69  0   0   60  249 211 64  0   64  6   36  176 169 254 100 29  169 254 100 30  128 1   0   21  5   142 65  189 0   0   0   0   160 2   22  208 149 45  0   0   2   4   5   180 4   2   8   10  0   0   184 110 0   0   0   0   1   3   3   1

packet data

__E<ùÓ@@_$°©þd_©þd_€___ŽA½ __Ð•-___´___

¸n____

| Byte | Content | Explanation |
| --- | --- | --- |
| IP Header |  |  |
| 1 | 69 | 69 = 0100 0101 0100 = 4 = Version of IP 0101 = 5 - Header length (4*5) = 20 bytes |
| 2 | 0 | Type of Service Used by some routers to prioritise packets i.e. some given higher precedence than others |
| 3/4 | 0 60 | Packet size in number of bytes 0 60 = 00000000 00111100 = 60 |
| 5/6 | 249 211 | Identification of specific datagram Unique for each packet – often just incremented by one. |
| 7/8 | 64 0 | 64 0 = 01000000 00000000 010 = Flags 010 Last bit if 0 = last fragment of packet Middle bit = Indicates that packet should not be fragmented. 0000000000000 = Fragmentation Offset |
| 9 | 64 | TTL – Time to live 64 – 01000000 Number of times a packet can go through a router before being discarded. |
| 10 | 6 | Protocol Number 1 = ICMP 6 = TCP 17 = UDP |
| 11/12 | 36 176 | Header Check Sum |
| 13/14/15/16 | 169.254.100.29 | IP Source Address |
| 17/18/19/20 | 169.254.100.30 | IP Destination Address |

| TCP Header |  |  |
| --- | --- | --- |
| 21/22 | 128 1 | Source Port 128 1 – 10000000 00000001 = 32769 Allows packets to be reordered |
| 23/24 | 0 21 | Destination Port 0 21 - 00000000 00010101 = 21 |
| 25/26/27/28 | 5 142 65 189 | Sequence Number 5 142 65 189 00000101 10001110 01000001 10111101 = 93209021 |
| 29/30/31/32 | 0 0 0 0 | Acknowledgement Number 0 0 0 0 00000000 00000000 00000000 00000000 = 0 |
| 33 | 160 | 160 = 10100000 1010 = 10 TCP Header Length in bytes = 10*4 = 40 bytes 0000 = Not used |
| 34 | 2 | 2 = 00000010 00 = Unused 000010 = Flags URG ACK PSH RST SYN FIN 000010 = SYN |
| 35/36 | 22 208 | 22 208 = 00010110 11010000 = 5840 Window Size – Buffer space limit |
| 37/38 | 149 45 | TCP Checksum |
| 39/40 | 0 0 | Urgent Pointer |
| 40 – 60 |  | Options – Sets Maximum Segment Size |
| End of TCP Header |  |  |

Other Protocols

| UDP Header |  |
| --- | --- |
| 21/22 | Source Port |
| 23/24 | Destination Port |
| 25/26 | Length of UDP Header and Data |
| 27/28 | Checksum |
| 29 onwards | Data |

| ICMP Header |  |
| --- | --- |
| 21 | Type 8 – echo 0 – echo reply |
| 22 | Code |
| 23/24 | Checksum |
| 25/26/27/28 | Other Information |
| 29 onwards | Data |